Description of JSON Configuration Parameters of the Extension Boards
# Root Items
- NAME: Name of the extension board
- DESC: Description of the extension board
- VER: Version of the extension board
- PD: Production date of the extension board
- PRMS: List of parameters supported by the board
  - NAME: Name of the parameter, e.g., “Current limit”
  - VLIST: List of the selectable parameter values, e.g., ["0.5A","1A","2A","3A","5A"]
- PROPS: List of properties of the board
  - NAME: Name of the parameter, e.g., “Maximum output current”
  - VAL: Value of the parameter, e.g., “3A”
- PINS: List of board pins (order of pins (sorted by ‘NUM’ field) matters but gaps are allowed between pin definitions anywhere). If a pin is not used, but adjacent pins serve the same function, the unused pin should be defined and aligned with the function of the adjacent pins.
  - NAME: Name of the pin
  - NUM: Number of the pin (1 .. 12)
  - FIDX: Reference to function (index of the FUNCS array)
- FUNCS: List of board functions
- NAME: Function name
- DESC: Function description
- GPIOS: List of Tasmota I/O channels used by the function
  - CHID: Channel ID (0..5). It will be mapped to a real GPIOx of Tasmota GPIO configuration.
  - OPT: Identifier of the GPIO option. It will be mapped to an existing Tasmota GPIO option. See “Table of GPIO options”.
  - OPTIDX: Option index, e.g., For Relay6 it is 5, for Relay8 it is 1. The index in Tasmota is calculated as ext_board_id(0..3) * 6 + OPTIDX.
- PRMS: List of parameter references and actual values
  - PIDX: Reference to the parameter (index of the PRMS array)
  - ACTIDX: Index for the actual value from VLIST.
- PROPS: List of indexes from PROPS array.
Table of GPIO options:
Option ID	Name	Tasmota GPIO name (base)	Tasmota GPIO ID (base)
0	Relay	GPIO_REL1	224
1	Bistable Relay	GPIO_REL1_BI	9312
2	PWM	GPIO_PWM1	416
3	Input	GPIO_INPUT	7648

# Examples