Description of JSON Configuration Parameters of the Extension Boards
# Root Items
- NAME: Name of the extension board
- DESC: Description for extension board
- VER: Version of the extension board
- PD: Production date of the extension board
- PRMS: List of parameters supported by the board
  - NAME: Name of the parameter, e.g., “Current limit”
  - VLIST: List of the selectable parameter values, e.g., ["0.5A","1A","2A","3A","5A"]
- PROPS: List of properties of the board
  - NAME: Name of the parameter, e.g., “Maximum output current”
  - VAL: Value of the parameter, e.g., “3A”
- PINS: List of board pins
  - NAME: Name of the pin
  - NUM: Number of the pin (1 .. 12)
  - FIDX: Reference to function (index of the FUNCS array)
- FUNCS: List of board functions
- NAME: Function name
- DESC: Function description
- TYPE: Peripheral identifier of this function, see “Table of board functions”. The value of this object is the ‘Type ID’ from the table.
- GPIOS: List of Tasmota I/O channels used by the function
  - CHID: Channel ID (0..5). It will be mapped to the real GPIOx of Tasmota GPIO configuration.
  - OPT: Identifier of the GPIO option. It will be mapped to Tasmota GPIO option. See “Table of GPIO options”.
- PRMS: List of parameter references and actual values
  - PIDX: Reference to the parameter (index of the PRMS array)
  - ACT: Actual value
- PROPS: List of properties (indexes of the PROPS array)
Table of board functions:
Type ID	Name
1	Digital output
2	Digital input
3	Analog input
4	Analog output
5	PWM output

Table of GPIO options:
Type ID	Name
1	Relay
2	Relay_b
3	PWM
4	Input

# Examples