Description of JSON Configuration Parameters of the Extension Boards
# Root Items
- NAME: Name of the extension board
- DESC: Description for extension board
- VER: Version of the extension board
- PD: Production date of the extension board
- PRMS: List of parameters supported by the board
  - PRM_x: Parameter with an ID (x)
    - NAME: Name of the parameter, e.g., “Current limit”
    - PLIST: List of the parameters, e.g., ["0.5A","1A","2A","3A","5A"]
- PROPS: List of properties of the board
  - PR_x: Property with an ID (x)
    - NAME: Name of the parameter, e.g., “Maximum output current”
    - VAL: Value of the parameter, e.g., “3A”
- IOCH: Description of the I/O channels on the board
- NAME: Name of the I/O channel
- DESC: Description for the I/O channel
- POS: I/O pin index, values are: 1 - 6
- TYPE: Type of the I/O, it can be:
  - 1: simple output
  - 2: simple input
  - 3: PWM output
  - 4: Latching relay set output
  - 5: Latching relay reset output
- PRMS: List of parameters and actual values, e.g., {{“PREF”:“PRM_1”}, {“ACT”:”1A”}},
  - PREF: Name of the parameter
  - ACT: Actual value
- PROPS: List of properties, e.g., [“PR_1”, “PR_2”]
# Examples